Technical specifications

Walking Test EVO

Range: ±1050V

Resolution: 1V

Accuracy: ±5% o ±5V

Input resistance: 10^14Ω

Humidity measurement:

Range: 1 to 95%RH

Resolution: 0.1%RH

Accuracy: ±2%RH (a 25°C, 10%~90%RH), ±3%RH (a 25°C, 1%~10%RH, 90%~95%RH)

Temperature measurement:

Range: -20°C to +60°C

Resolution: 0.1°C

Accuracy: ±1°C

Display: graphic LCD 128x64pixel, 68x51mm.

Power: 6 LR6 1,5V alkaline cells

Dimensions: 243x130x60mm (instrument) - Ø35x130mm (probe)

Weight: 650g (instrument) - 250g (probe)

Datalogger

In the internal memory of the instrument can be logged till to 10 graphs.

Sample rate: 200Hz

Max total graphs duration: 2minutes and 30 sec

Interface: USB