Technical specifications

SRM-1064 Surface Resistance Meter

Resistance measurement:

- Test voltage: 10V, 100V, 250V, 500V or AUTO (10V if R<100KΩ and 100V if R>100KΩ in accordance with IEC61340-5-1)

- 10V : from 1KΩ to 50GΩ (±5% ±0.6% per GΩ)

- 100V : from 100KΩ to 1TΩ (±5% ±0.06% per GΩ)

- 250V: from 500KΩ to 1TΩ (±5% ±0.045% per GΩ)

- 500V: from 1MΩ to 1TΩ (±5% ±0.03% per GΩ)

Humidity measurement:

- Range: 1 to 95%RH

- Resolution: 0.1%RH

- Accuracy: ±2%RH

Temperature measurement:

- Range: -20°C to +60°C

- Resolution: 0.1°C

- Accuracy: ±1°C

- Display: graphic LCD 128x64pixel, 68x51mm.

- Power: 6 LR6 1,5V alkaline cells

- Dimensions: 243x130x60mm

- Weight: 650g

Please ook the file section for more info.