Technical specifications

Profitest Prime Testing of Electrical Machines and Equipment

A broad-range measuring device permits use of the test instrument in all alternating and 3-phase electrical systems with voltages from 65 to 690 V and frequencies of 15.4 to 420 Hz, as well as direct current systems with voltages from 65 to 800 V.

- Voltage measurement up to 1000 V AC/DC

- Low-resistance measurement for protective and equipotential bonding conductors with 200 mA, as well as automatic polarity reversal and 25 A

- Insulation measurement up to 1000 V with rising ramp

- Measurement of internal system resistance and fault loop resistance with high test current up to 690 V AC / 800 V DC without tripping RCD types A and B

- Testing of tripping current and time to trip for RCCB types A, AC, F, B, B+, EV, MI and G/R, as well as SRCDs and PRCDs

- Combined RCD test with continuously rising ramp, time to trip, tripping current

- Testing of RCMs and IMDs

- Measurement of leakage and differential current with the PROFICLIP current clamp

- Measurement of temperature and humidity with a sensor

- Mains and battery operation (with limited functionality)

- Creation of individualized test sequences

- Push-print function - transmission of the measured value via Bluetooth/USB after measurement has been completed

- Bluetooth and USB interfaces

- Windows-based user software with database functionality