Technical specifications

AT-2816A / AT-2816B LCR Meter

Specification

Parameters; Cs-Rs,Cs-D,Cp-Rp,Cp-D,Lp-Rp,Lp-Q,Ls-Rs,Ls-Q,G-B,R-X,Z-θrad,Z-θdeg; . Monitor Parameters; Z, D, Q, θr, θd, R, X, G, B, Y, Vac, Iac, Δ, Δ%; . Accuracy; 0.05% ±5; . Frequency; 50Hz～200kHz; . Display Range; L: 0.00001μH - 999999H C: 0.00001pF - 999999μF R,Z: 0.00001Ω - 99.9999MΩ Q: 0.00001 - 999999 θ(deg): -90.0000°- 90.0000° θ(rad): -3.14159 – 3.14159 Δ%: -999.999% - 999.999% D:0.00001 ～ 9.99999; . Source Resistance; 30Ω 50Ω 100Ω; . Range; 9 ranges, Automatic, Manual, Nominal; . Display Max; 6 dgt, principle parameter: 999999; sub parameter: 999999; monitor parameter: 999999; . Signal Level; 0.01V - 2.00V (10mV Step); . Speed; 30 t/s, 10 t/s, 6 t/s, 3 t/s 1 - 256 times average is available; . Comparator; 14-bin sorting, 10-bin GD, 1-bin NG, 1-bin AUX, 2-bin principle parameter NG Count function: Max - 999999; . List Test; 10 groups frequency and level scanning test; . Adjustment; Open/Short frequency reset, 3 point frequency and load correction; . Files; 10 group files to save users' setting, 1 group to save system data real-time; . Interface; RS232C, ExHandler Interface, with standard USB disc interface (article 10000 data); . Others; LCR automatic selection, keypad lock, SCPI instruction set, true-color TFT-LCD display; . Power Suplly; Voltage: 90V AC - 250V AC Frequency: 50Hz - 60Hz Power: Max 20VA; . Size; 264mm(Width)x107mm(Height)x350 mm(Depth); 4kg; . Accessories; ATL501: Test cable ATL607: Test fixture ATL600: Short-circuit slice ATL801: 232 Communication cable; . Options; ATL608 SMD patch clamp ATL508: SMD patch test clip ATS2816B: Data acquisition software ATL508A: SMD patch test clip; .