Technical specifications

CEM DT-191A Temperature/Humidity Dataloggers

| Specifications |
| --- |
|  | DT-191A |
| Temp. range | -40 to 70℃/ -40 to 158℉ |
| Temp. accuracy | ±1℃/1.8℉ |
| Temp. resolution | 0.1℃/0.1℉ |
| Humidity range | 0 to 100%RH |
| Humidity accuracy | ±3.5%RH |
| Humidity resolution | 0.1%RH |
| Air pressure range |  |
| Air pressure accuracy |  |
| Air pressure resolution |  |
| Memory | 40020(20010 / channel) |
| Sample rate | 1min-24 hours |
| Battery life | 1years（Sample rate 1minute） |
| PDF report | Immediately USB fl ash disk PDF report |
| Analysis software | Windows XP/Vista/win7/win8/win10 |

| Features |
| --- |
|  | DT-191A |
| Temperature datalogger |  |
| Temperature and humidity datalogger | * |
| Temperature and air pressure datalogger |  |
| Immediately USB fl ash disk PDF report | * |
| Freely selectable sample rate 1 min to 24h | * |
| LCD Max Min display | * |
| Download collected data through USB interface | * |
| Battery life :up to 1 years (1 minutes sample rate ) | * |
| Alarm display if user-defi ned maximum/minimum value exceed | * |
| Analysis software used to view graph for logging data | * |

Size(HxWxD): 75mm x 35mm x 16mm

Weight: 50g