Technical specifications

MetraHit IM E-Drive All-in-One

Technical Features

- Installation resistance measurement up to 3.1 GΩ with interference voltage detection, test voltages: 50, 100, 250, 500 and 1000 V per EN 61557-2 / VDE 0413-2

- DAR: dielectric absorption rate, PI: polarization index

- 4-wire milliohm measurement with Kelvin connection and 200 mA or 1 A measuring current for precise measurement of extremely small resistances with a resolution of 1μΩ

- 2-wire Rlow measurement with 200 mA test current per EN 61557-4 / VDE 0413-4

- Short-circuited coil measurement

- Multifunctional instrument (V, A, Ù, F, Hz, %, RPM, °C/°F)

- TRMS AC / AC+DC measurement for current/voltage up to 10/100 kHz

- Low-pass filter can be activated AC, AC+DC

- Direct current measurement

- Current measurement with clamp sensors: The transformation ratio can be adjusted with the CLIP from 1:1 to 1:1000 and is taken into account in the amperage display.

- Capacitance measurement

- Precision temperature measurement °C, °F for RTD and TC-K sensors

- Diode measurement (Uflow up to 5.1 V) and continuity testing

- Acoustic signals

- Acquisition of min./max. values, DATA Hold

- Data logger thanks to integrated memory module and real-time clock, for individual measurements as well

- Push/print function transfers measured values to application software by simply pressing a key

- Programmable sequences for test routines

- Color graphic display

- Modular power supply: standard quick-change rechargeable lithium battery, optional WPC module for inductive charging and mains module with USB port, change without interrupting the measuring circuit thanks to touch-protected module socket

- Automatic blocking sockets (ABS) for the current input

- Remote probe with START (ISO) and STORE keys

- Housing with IP 52 protection, dust and splash protected, replaceable rubber holster

- Interfaces: Bluetooth or WIFI integrated, USB with optional mains module

- IZYTRONIQ Windows software for documentation, preparation of test reports and graphic evaluation of measurements

Please look the file section for more info.