Technical specifications

CEM DT-898 TRMS Multimeter with Thermal Camera

| Specifications |
| --- |
| Thermal Imager | 898/898A | 889/889A |
| IR Resolution | 80x60 pixels | 32x32 pixels |
| Field of view(FOV) | 17°x17° | * | 40°x40° |
| Thermal sensitivity/NETD | <0.08℃/80mK | * | * |
| Image frequency | 50Hz | * | 9Hz |
| Object temperature range | ﹣20 to 260℃(﹣4 to 500℉) | * | ﹣20 to 300℃(﹣4 to 572℉) |
| Spectral range | 8-14μm |
| Color palettes | IRON/Rainbow/Grey/Grey Inverted |
| Accuracy | ±2℃(±3.6℉) or ±2% of reading |
| True RMS Multimeter Functions |
| Function | Max Range | Basic Accuracy |  |  |
| Voltage DC | 600V | ±0.5% | * | * |
| Voltage AC | 600V | ±1.0% | * | * |
| Current DC | 10A | ±1.5% | 898 | 889 |
| Fork clamp DC current | 100A | ±2.0% | 898A | 889A |
| Current AC | 10A | ±2.0% | 898 | 889 |
| Fork clamp AC current | 100A | ±2.5% | 898A | 889A |
| Resistance | 40MΩ | ±1.0% | * | * |
| Capacitance | 4000μF | ±3.0% | * | * |
| Frequency | 10kHz | ±1.0% | * | * |
| Duty Cycle | 99.9% | ±1.2% | * | * |
| Diode Check | * | * |
| Continuity Test | * | * |