Technical specifications

DT-6650 Multifunction Installation Tester

| Specifications |
| --- |
| Insulation |
| Terminal Voltage | Range | Max Resolution | Accuracy | Test Current | Short circuit current |
| 125V (0% ~ +10) | 0.125~4000MΩ | 0.001MΩ | ±(2%+10) | 1mA@load 125kΩ | ≤1mA |
| 250V (0% ~ +10) | 0.250~4000MΩ | 0.001MΩ | ±(2%+10) | 1mA@load 250kΩ | ≤1mA |
| 500V (0% ~ +10) | 0.500~4000MΩ | 0.001MΩ | ±(2%+10) | 1mA@load 500kΩ | ≤1mA |
| 1000V (0% ~ +10) | 1.000~4000MΩ | 0.001MΩ | ±(3%+10) | 1mA@load 1MΩ | ≤1mA |
| Low OHM |
| Range | Resolution | Accuracy | Max. open Circuit Voltage | Overload Protection |
| 4.000Ω | 0.001Ω | ±(1.5%+30) | 5.8V | 250Vrms |
| 40.00Ω | 0.01Ω | ±(1.5%+3) |
| 400.0Ω | 0.1Ω |
| Continuity Beeper |
| Range | Resolution | Operation Resistance | Max. open Circuit Voltage | Overload Protection |
| Continuity | 0.01Ω | Resistance≤35Ω | 5.0V±1VDC | 250Vrms |
| Short circuit current | ≥200mA |
| LOOP Resistance |
| L-PE (Hi-Amp) |
| Range (Ω) | Max. Resolution (Ω) | Accuracy |
| 0.00~999 | 0.01 | ±(4% of reading+6 digits) |
| L-PE(No Trip): Measuring Current:15mA / Range of the Voltage Used: 195V a.c.~260V a.c.(56,60Hz) |
| Range (Ω) | Resolution (Ω) | Accuracy |
| 0.00~999 | 0.01 | ±(5% of reading+6 digits) |
| L-N: Measuring Current:2.0A / Range of the Voltage Used:195V a.c.~260V a.c.(56,60Hz) |
| Range (Ω) | Max. Resolution (Ω) | Accuracy |
| 0.00~999 | 0.01 | ±(4% of reading+4 digits) |
| RCD Testing |
| Test current | Accuracy |
| x1/2, x1, x2, x5 | 1.5%~ -9% |
| Voltage and Frequency |
| Measurement Range (V)/ AC-DC | Resolution | Accuracy |
| 80-500V/(45-400Hz) | 1V | ±(2% of reading+2 digits) |