Technical specifications

DT-6605 High Voltage Insulation Tester

| Specifications |
| --- |
| Function | Insulation resistance | Voltage | Resistance |
| Range | 500V | 1000V | 2500V | 5000V | AC/DCV |  |
| Measuringrange (Auto ranging) | 0~6.000MΩ 6~60.00MΩ 60~600.0MΩ 600~6000MΩ | 0~6.000MΩ 6~60.00MΩ 60~600.0MΩ 600~6000MΩ | 0~60.00MΩ 60~600.0MΩ 0.6~6.000GΩ 6~60.00GΩ | 60~60.00MΩ 60~600.0MΩ 0.6~6.000GΩ 6~60.00GΩ | 0~600.0V (50~1kHz) | 0~600.0Ω 600~6000Ω |
| Accuracy | ±5%rdg ±3dgt ; ±20% (>6GΩ or more) | ±1.5%rdg ±5dgt | ±1.5%rdg ±10dgt |
| Short Circuit Current | 1.3mA approx | - |
| Rated test Current (at load Resistance) | 1mA-1.2mA 0.5MΩ | 1mA-1.2mA 1MΩ | 1mA-1.2mA 2.5MΩ | 1mA-1.2mA 5MΩ | - |
| Open circuit voltage | 500VDC/+20%-0% | 1000VDC/+20%-0% | 2500VDC/+20%-0% | 5000VDC/+20%-0% | - |
| Continuity check | Buzzer sounds at 50Ω |
| Display | 6000 Counts |
| Current consumption | About 1000mA (During measurement) | 25mA approx. |
| Withstand Voltage | 5320V AC for 5 seconds |
| Safety standard | IEC 61010-1 CAT IV 600V Pollution Degree 2 |
| Power supply | DC12V : R14 x 8 |
| Dimensions | 198 ( L) x 148 (W) x 86 ( D) mm |
| Weight | 1438g approx. |
| Accessories | Test leads, Instruction Manual and 120V/250V AC adaptor |