Technical specifications

MetraHit IM Tech All-in-One

Technical characteristics

- 4-wire milliohm measurement with Kelvin connection and 200 mA or 1 A measuring current for precise measurement of extremely small resistances with a resolution of 1

- Multifunctional instrument

- TRMS AC / AC+DC measurement for current/voltage up to 10/100 kHz

- AC, AC+DC low-pass filter

- Direct current measurement

- Current measurement with clamp sensors: The transformation ratio can be adjusted with the CLIP from 1:1 to 1:1000 and is taken into account in the amperage display.

- Capacitance measurement

- Precision temperature measurement - °C, °F for RTD and TC-K sensors

- Diode measurement (Kflow up to 5.1 V) and continuity testing

- Acoustic signals

- Acquisition of min./max. values, DATA Hold

- Data logger thanks to integrated memory module and real-time clock, for individual measurements as well

- The push/print function transfers measured values to application software by simply pressing a key

- Optional programmable sequences for test routines

- METRALOG APP for Android OS

- Color graphic display

- Modular power supply: standard quick-change rechargeable lithium battery and mains module with USB port, change without interrupting the measuring circuit thanks to patented touch-protected module socket

- Automatic blocking sockets (ABS) for the current input

- Housing with IP 52 protection, dust and splash protected, replaceable rubber holster

- Bluetooth integrated, USB with optional mains module

- IZYTRONIQ Windows software for documentation, preparation of test reports and graphic evaluation of measurements