Technical specifications

Profitest H+E Easy Check

Technical Characteristics

- Automatic function tester for AC charging points

- Also for AC charging points with permanently attached cable

- Easy to use – even for laypersons

- Automatic test sequence saves time and money

- Results appear at the display in plain text

- Error display with results for forwarding to service personnel

- USB port for charging the battery

Particularities

- Automatic function tester for AC charging points in charging mode 3

- Simulation of an EV at the charging point with type 2 plug inlet and charging points with permanently attached cable

- Verification of values for 20 A and 32 A cables

- Testing of vehicle statuses A, B and C, phases, tOFF (status E), rotating field and duty cycle

- Results appear at the display in plain text

- Error display with results for forwarding to service personnel (internal memory for momentary measured value)

- USB port for charging the battery