Technical specifications

Seculife PS100 Patient Simulator for ECG

Technical characteristics

ECG

30, 60, 120 and 240 BPM

Sine waves: 10, 60 and 100 Hz

Square waves: 0.125 and 2 Hz

Triangle waves: 2 Hz

High level output: 1 V p-pAmplitude tolerance: ± 2%

- Frequency tolerance: ± 0.5% of the specification

- Integrated terminals for continuity test (lead test)

- Front panel resistant to disinfectant wipes

Terminals

10 outputs for electrode plugs (2 to 4 mm ), snap fasteners and clips

- 1 output with 1 V signal strength for ECG devices without amplifier

Power supply

- 9 V battery and low battery display

for more info please look the file section.