Technical specifications

Seculife PS200 Multi-patient Simulator for ECG

Tehnical Characteristics

EKG

30, 60, 80, 120, 180, 240 and 300 BPM

Sine waves: 0.1, 0.5, 5, 10, 40, 50, 60 and 100 Hz

Square waves: 0.125 and 2 Hz

Triangle waves: 2 Hz

High level output: 1 V p-p

- Amplitude tolerance: ± 1%

Respiration

- Apnea, 15, 20, 30, 40, 60, 80, 100, 120 BrPM

Blood pressure

- Static 0, 20, 40, 80, 100, 200, 250, 300 mmHg

Temperature

30, 37, 40°C

- YSI 400 and 700

SpO2 Simulation

30 to 300 BPM

- 80, 90 and 97%

- Integrated terminals for continuity test (lead test)

- Front panel resistant to disinfectant wipes

Terminals

10 outputs for electrode plugs (2 to 4 mm ), snap fasteners and clips

1 output with 1 V signal strength for ECG devices without amplifier

- Mini DIN terminals (compatible with many blood pressure cables)

Power supply

9 V battery or external power pack

- Low battery display and battery life display

Please look the file section for more info.