Technical specifications

Seculife PS300 Multi-patient Simulator for ECG

Product Highlights

EKG

30, 40, 45, 60, 80, 90, 100, 120, 140, 160, 180, 200, 220, 240, 260, 280 and 300 BPM

Sine waves: 0.1, 0.5, 5, 10, 40, 50, 60 and 100 Hz

Square waves: 0.125 and 2 Hz

Triangle waves: 2 Hz, 2.5 Hz

Haver triangle waves: 30, 60, 80, 120, 200 and 250 BPM

High level output: 1 V p-p

- Amplitude tolerance:± 1%

Respiration

- Apnea, 15, 20, 30, 40, 60, 80, 100, 120 BPM

Static blood pressure

- -10, -5, 0, 20, 40, 50, 60, 80, 100, 150, 160, 200, 240, 250, 300, 320 and 400 mmHg

Temperature

0, 24, 30, 37, 40°C

- YSI 400 and 700

SpO2 Simulation

30 to 300 BPM

- 80, 90 and 97%

- Integrated terminals for continuity test (lead test)

- Front panel resistant to disinfectant wipes

Terminals

10 outputs for electrode plugs (2 to 4 mm ), snap fasteners and clips

1 output with 1 V signal strength for ECG devices without amplifier

- Mini DIN terminals (compatible with many blood pressure cables)

Power supply

9 V battery or external power pack

- Low battery display and battery life display