Technical specifications

CEM IR-77H Pocket InfraRed Thermometer

Specifications

- Range: -30°C - 270°C / -22°F - 518°F

- Response Time: Less than 1 second

- Resolution: 0.1ºC/ºF

- Basic Accuracy: ±2% or ±2ºC/±4ºF

- Optical Resolution: 6:1

- Emissivity: Fixed at 0.95

- Battery: 1.5V AAA battery x 2