Technical specifications

AT826 Handheld LCR Meter

Specifications

- Test Functions: L,C,R,Z

- Accuracy: 0.2%

- Measurement Frequency: 100Hz, 120Hz, 1kHz, 10kHz, 100kHz

- Measurement Speed: 4 times/s, 1.5 times/s

Display Range

L: 0.01uH-9999H

C: 0.01pF - 9999uF

R,Z: 0.0001Ω - 99.99MΩ

D:0.0001–9.999

- Q:0.0001~999.9

- Source Resistance: 100Ω

- Display Reader: 49999

- Signal Level: 0.6Vrms, ±10% accuracy

- Trigger Mode: Internal

- Comparator: 1 sets, compare main parameters

- Comparator Mode: SEQ/ABS/PER

- Adjustment: open/short clear zero

- Files: USB storage

- Interface: USB-HID

- Protocol: SCPI

Other Functions:

- Touch screen, USB-HID communication, compatible SCPI, English & Chinese language, adjustable back light, auto power off(APO)

Power Supply:

input: 100-240V，50Hz, 0.35A,

- output:9V 1A DC

- Dimension & Weight: 90*195*35.5mm / 400g