Technical specifications

Mavo-Spot 2 USB Luminance Meter

Technical Data

- Illuminance [Lux]: 0.1 … 99 900 lx - optional reflection standard, classified

- Luminance: 0.01 cd/m² … 99 990 cd/m² / 0.01 fL … 30 000 fL

- Measuring ranges: 4

- Measuring ranges selection: Automatic/Manual

- Measuring rate: 2 per second

- Measuring method: Distance measurement with 1° measuring angle, 1 m up to ∞, optional contact measurement with measuring probe

- Measuring sensor: Silicon photocell with V(λ) filter

- Measured value memory: Up to 1000 individual values or 10 groups with 100 individual values each (switchable)

- Error limit – V(λ) adapted (f1‘), typical: < 3 %

- Error limit – overall error, typical: ≤ 8 %

- Accuracy: ±2.5 % of read out ± 2 digit

For more technical info please look the file section.