Technical specifications

AT-5800 Battery Comprehensive Tester

Specification

Internal Resistance

Accuracy: 0.5%

Measurement Range: 0.0001mΩ - 300.00Ω, 6 ranges Auto or Manual

Signal Source: AC 1kHz, 20ppm

Measurement Speed: SLOW: 3 times/s, FAST: 20 times/s

- Adjustment: Short-circuit Clear Zero

Battery Voltage

Accuracy: 0.01%

- Measurement Range: 0.00001V - 80.0000VDC, 2 ranges Auto or Manual

Power Supply

Rated Output: 30V, 15A, 100W

Voltage Resolution: 0.01V

Current Resolution: 0.001A

Power Resolution: 0.01W

Ripple Voltage: <5mVrms

Ripple Current: <5mArms

Load Regulation: Voltage:< 0.01%+3mV, Current: < 0.01%+3mA

Line Regulation: Voltage:< 0.01%+3mV, Current: < 0.01%+3mA

Programming Accuracy: Voltage:< 0.05%+10mV, Current: < 0.1%+2mA

- Read Back Accuracy: Voltage:< 0.05%+10mV, Current: < 0.1%+2mA

DC Electronic Load

Rated Input: 30V, 15A, 100W

CC: 0-3A: Resolution:0.0001A; Accuracy: ±0.1%±6dgts, 0-15A: Resolution:0.001A; Accuracy: ±0.2%±6dgts

CV: 0~30V: Resolution:0.001V Accuracy: ±0.05%，±6dgt

CP: 0~100W: Resolution:0.1W Accuracy: ±1%，±dgt

CR: 0~4kΩ: Resolution:1Ω Accuracy: ±1%，±2dgt

- Short Circuit: Current: ≈15A

Battery Capacity Test

Capacity Test Range: 0.001 - 9999.9AH, Resolution 0.001AH

- 1C Current charge&discharge: 3 - 4 hours

Comprehensive Test: Quick test and sorting of the characteristics of the battery with protection board, the test item can be edited by user.

Static Test: Test all functions: 2s

Battery Activation: Take the battery out of sleep or over-discharge protection state

Voltage and Internal Resistance Four-terminal test, accurately test 1KHz AC internal resistance and battery static voltage

Battery Charge The tester charges the battery. When the test time is reached, the actual voltage of the test battery is compared with the set upper and lower limits.

Battery Over-charge: To charge the battery according to the step current and step time set by the user, and at the same time detects whether the current is cut off, the battery charging protection current is tested, and the upper and lower limits are compared to determine whether the battery charging overcurrent protection function is normal

DC Internal Resistance: DC Load module get battery no-load and load voltage, convert DC internal resistance.

The test range: 0 - 1000mΩ

Battery Discharge: To discharge the battery. After the test time is reached, the actual voltage of the test battery is compared with the set upper and lower limits.

Battery Over-discharge: To discharge the battery according to the step current and step time set by the user, and at the same time detects whether the current is cut off, the battery discharge protection current is tested, and the upper and lower limits are compared to determine whether the battery discharge overcurrent protection function is normal.

Short Circuit: To load the maximum current within the set time, simulates the short-circuit condition, and detects whether the current is cut off at the same time. The short-circuit protection time of the battery is tested and compared with the set upper and lower limits to determine whether the battery short-circuit protection function is normal or short-circuited.

- Battery Recovery: After the short circuit test, over-charge test, and over-discharge test, the battery may be in a protected state, and the recovery test can determine whether the battery is back to normal.

- Trigger Mode: Internal, External and Remote

- Interface: Handler, RS-232, USB

- Display: 5 inch TFT-LCD true color display, full touch operation

- Power Supply: 220VAC,150W MAX

- Dimension: 300 x 130 x 420 mm

- Mass: 5kg