Technical specifications

HTI HT-06 Thermal Imager with Wi-Fi (256x192)

Infrared detector type: Vanadium Oxide Uncooled Infrared Focal Plane

Infrared resolution: 256x192

Infrared response band: 8 to14μm

Cell size: 12μm

NETD: ＜50mK @ F#1.0

Thermal imaging frame rate: ≤25Hz

Lens focal length: 3.2mm

Emissivity setting: Adjustable from 0.01 to 1.00

Field angle: 35°×27°

Focus mode: Non-heating fixed focus lens

Temperature measurement range: -20℃ to +550℃(-4 ℉ to 1022 ℉)

Measurement accuracy: ±2℃or ±2%

Temperature measurement mode: Center point/hot and cold spot tracking

Color palette: Rainbow, iron, cold color, white hot,

black hot

Display size: 2.8-inch(240×320)

Image display mode: Infrared/visible light/dual light fusion

Lighting system: LED fill light

Device storage: Built-in 4G eMMC (user available storage space is about 3G)

Storage Image/Video Format: JPG/MP4

Image/video export method: USB connection to computer export

Image analysis function: Support offline analysis on PC

Menu language: English、Chinese、Italian、German

Battery Type: Removable Rechargeable Lithium Battery (18650)

Battery capacity: 2000mAh

Working time: 2 to 3 hours

Power interface: Micro USB

Power configuration: 5 minutes / 20 minutes / no automatic shutdown

Work temperature: 0℃ to +45℃ (32 ℉ to 113 ℉)

Storage temperature: -20℃ to +60℃ (-4℉ to 140℉)

Relative humidity: 10% to 85%RH (non-condensing)

Product weight: 389g

Product size: 96mm×72mm×226mm

WIFI: YES