Technical specifications

EVSE-200 Electric Vehicle Charging Station EVSE Adapter

Functions

- PE Pre-Test: With this safety feature, the PE conductor can be tested for the possible presence of hazardous voltage to earth.

- Proximity Pilot (PP) status "Cable Simulation": With the PP Status rotary switch, the adapter can simulate various current capacities of charging cables.

- Control Pilot (CP) status "Vehicle Simulation": With the CP Status rotary switch selector, various charging states can be simulated.

- Simulation of CP fault "E"

- PE fault simulation (Earth fault)

General Characteristics

- Suitable for car charging stations with charging mode 3.

- EV-connectors for type 2 and type 1.

- L1, L2, L3, N and PE measurement terminals are available for connecting to devices such as multifunctional installation testers to perform safety and functional tests.

- CP signal output terminals to control the communication between the adapter (simulated electric vehicle) and the charging station.

Device Specifications

- Separate phase indicator with three LED lamps to easily check whether voltage is present.

- Mains socket with the possibility to connect an external load to check the correct operation of the electricity meter.

- IP 54 rating - Protection against dust and splashing water.