Technical specifications

Metraline MF Multifunctional Installation Tester

Technical characteristics

- Loop and line impedance measurement with RCD

- Low-impedance measurement with 200 mA, automatic polarity reversal

- Earthing measurement, 3-pole, 4-pole and Wenner (optional with E-Set Basic)

- Insulation resistance measurement up to 1000 V, adjustable

- Testing of RCD/FI for types A, AC, B, B+, F and auto-sequence

- Testing of RDC-DD with 6 mA DC for e-charging points

- Voltage measurement (TRMS), phase sequence and frequency

- Help diagrams for each measuring function and acoustic signals during measurement

- Data management, storage of 1000 measured values

- METRAreport software for documentation

- USB interface, IP 40, CAT III 600 V / CAT IV 300 V