Technical specifications

AT-9600 Ground Resistance Meter

Specifications

- Measurement Functions: Ground resistance

- Interface: RS232/RS485, HANDLER, USB

- Standard Configuration: AC 5A-40A

- Comparator: Upper and lower limit sound and light alarm

- Protect Function: Over-voltage protection

- Ground Impedance: 0 - 600mΩ accuracy ±(2%× Read the numerical +5 dgt ) resolution 0.1 mΩ

- Current Setup Range: AC 5A - 40A，accuracy ±(2%× reading +5 dgt ), resolution 0.1A

- Power Supply: AC 220V 50Hz, power <200W

- Dimension & Weight: 250×120×320mm, 10kg

- Accessories: power cable, RS232 communication cable, ATL900A test clamp

Please look the file section for more info.