Technical specifications

The CEM DT-173 Sound Level Datalogger

General Features

- Compliant Standard: IEC 61672-1 Class 2

- Accuracy: +/-1.4dB

- Frequency Range: 31.5Hz - 8kHz

- Dynamic Range: 50dB

- Measurement Range: 30dB - 130dB

- Data Memory 129,920 pieces

- Sampling: 1 second to 24 hours

- Frequency Weighting A and C

- Time Weighting: Fast (125ms) and Slow (1 second)

- Microphone 1/2-inch electret condenser microphone

- Operation Indicator: Green LED flash

- Memory Full Warning: Yellow LED flash

- Data Transfer Interface: USB

- Battery: 3.6V, 14250 or 1/2AAA

- Operating Temperature: 0 - 40°C

- Operating Humidity: 10% - 90% RH

- Dimensions: 130 x 30 x 25 mm

- Weight: 20 grams

Please look the file section for more info.