Product Descriptions

WST 1860 Wrist Strap and Footwear Tester

Test station for checking personnel grounding connection of wrist straps and footwear, according to the IEC 61340-5-1.

Separate testing of left and right shoe; the test is executed at 50V or 100V to provide more accuracy.

A relay output allows access to ESD Protected Area.

Internal battery supplied 9V or external 9Vdc.

ISO9000 traceable certificate is included.

The personnel grounding test station can work in 4 modes:

1) Simultaneous measurement of wrist straps and footwears.

2) Wrist straps only measurement

3) Footwears only measurement

4) HandsFree mode (if the serial measure of the two footwears pass the test then the internal relay enables the gate to the EPA area)

High efficiency led displays.

Fully programmable by keyboard.

Product Code: WST-1860