Product Descriptions

WST 1925 Wrist Strap and Footwear Tester

The Test Station EVO records and documents the parameters of the ESD protection of the personnel(wriststrap and footwears).

It can be used both wall-mounted or in a console configuration.

Technical features:

- Measurement of bracelets and footwears according to IEC61340-5-1

- Up to 1000 different users identified through fingerprint recognition or manual recognition (entering the ID number)

- Fingerprint recognition 1,5 sec

- Datalogger can store data for the last 10000 access (date and time, user name and ID, the resistance values of the bracelet and shoes, etc ...)

- Control footwear separate (left and right)

- Relay output for controlling the opening of the access door to the EPA

- LCD display with blue backlight 160 x 104 pixels, 74 x 46mm viewable area

- Beep to indicate clearly PASS or FAIL test of the protections

- Voltage Test selectable to 50V or 100V.

- Programmable tresholds

- ISO9000 Traceable Calibration Certificate included

- Program to manage the data recorded included in the Test Station EVO (compatible with Win XP/7/8/10)

Product Code: WST-1925