Product Descriptions

MetraPort 40S TRMS Folding Multimeter for Automotive Service

METRAport 40S digital multimeters are very well suited for universal use in general electrical engineering, electronics applications and for automotive service.

Ideal reading angle adjustment is made possible by the tilt stand, and when suspended from the neck strap both hands are free for performing measurements. The instrument is switched off automatically when folded closed, and the display and the control panel are protected against damage.

Precision multimeter (V, A, , F, Hz, %, °C / °F),

resolution: 10 μV, 10 nA, 10 mΩ, ± 31,000 digits (4¾-place)

TRMS measurement for V AC and I AC to 10 kHz

DC measurement of 10 nA to 10 A via a single socket and a resetable fuse (auto-fuse), overload and blown fuse indicators

Current measurement with current sensor clamps:

The transformation ratio is adjustable from 1 mV:1 mA to

1 mV:1 A, and is accounted for by the display.

Temperature measurement with automatic Pt sensor recognition

Temperature measurement with type K thermocouple

Capacitance and diode measurement

Frequency measurement via V AC or I AC to 10 kHz

Frequency and keying ratio measurement at 2 to 5 V signals up to 1 MHz

RPM Measurement with Inductive Sensor (accessory)

Automatic and manual measuring range selection

Large backlit digital display with additional analog scale

Measured value storage and min./max. recording

USB interface

DAkkS certificate and 3 year guarantee

Product Code: M234D