Product Descriptions

SRM-1064 Surface Resistance Meter

The GIGALAB EVO multi-voltage high resistance meter made by Iteco, is a portable, accurate, and versatile instrument designed for ESD measures: resistance between two points, surface to ground, and surface resistivity as defined in IEC61340-5-1.

Resistance measurement:

- Test voltage: 10V, 100V, 250V, 500V or AUTO (10V if R<100KΩ and 100V if R>100KΩ in accordance with IEC61340-5-1)

- 10V : from 1KΩ to 50GΩ (±5% ±0.6% per GΩ)

- 100V : from 100KΩ to 1TΩ (±5% ±0.06% per GΩ)

- 250V: from 500KΩ to 1TΩ (±5% ±0.045% per GΩ)

- 500V: from 1MΩ to 1TΩ (±5% ±0.03% per GΩ)

Humidity measurement:

- Range: 1 to 95%RH

- Resolution: 0.1%RH

- Accuracy: ±2%RH

Temperature measurement:

- Range: -20°C to +60°C

- Resolution: 0.1°C

- Accuracy: ±1°C

- Display: graphic LCD 128x64pixel, 68x51mm.

- Power: 6 LR6 1,5V alkaline cells

- Dimensions: 243x130x60mm

- Weight: 650g

By pressing a dedicated button it’s possible to quickly switch between viewing formats natural to exponential and vice versa.

Internal memory where the data of 100 measures can be stored. The data stored for each measurement are:

– Resistance value

– Voltage used for the measurement

– Humidity detected during measurement

– Measured temperature during measurement

Fully settable acoustic alarm.

Product Code: SRM-1064