Product Descriptions

Metracal MC Universal Calibrator, Simulator and Multimeter

The new, compact multifunction process calibrator convinces by ruggedness, simple handling, highest functionality, precision and PC system ability.

The METRACAL MC rationalizes measuring, calibrating and revision work in the chemical process, laboratory and development, in the production area of electronic measurand transducers and at comparison and calibration of metrological components.

- Universal calibrator, simulator and multimeter: mA / mV... V / °C (Pt100/1000, Ni100/1000, thermocouples: J, L, T, U, K, E, S, R, B, N) / 30 ... 2000 Ω

- Dual mode ¡V simultaneous calibration and measurement (U / I)

- Measuring and encoding in absolute terms and as percentage (scaled)

- Memory for measurement results: 16 MBit

- Frequency and pulse run generators: 1 Hz to 2 kHz

- Ramp and staircase functions

- METRAwin µ90-2 interface and calibration software

- Transmitter simulator (sink: 0... 24 mA)

- DAkkS calibration certificate included

- Rugged, EMC compliant design

- Precision multimeter (V, A, Ω, F, Hz, °C / F)

- 30,000 (60,000) digits and triple display

- TRMS AC measurement to 20 kHz

Product Code: M245A