Product Descriptions

ProfiTest MPro Installation Test Devices

A broad-range measuring device allows for use of the test instrument in all alternating and 3-phase electrical systems with voltages from 65 to 500 V and frequencies of 15.4 to 420 Hz.

- Loop and line impedance measurement

- Measurement of insulation resistance using nominal voltage, with variable or rising test voltage

- Low-resistance measurement

- Earth resistance measurement

- Standing-Surface Insulation Measurement

- Universal connector system

Features

- Selectable user interface language

- Memory (database for up to 50,000 objects)

- Automatic test sequence function

- RS 232 port for RFID/barcode scanner

- USB port for data transmission

- ETC user software for PC

- Measuring category: CAT III 600V / CAT IV 300V

- DAkkS calibration

Scope of Delivery

- 1 Test instrument

- 1 Earthing contact plug insert (country-specific)

- 1 2-pole measuring adapter and 1 cable for expansion into a

- 3-pole adapter (PRO-A3-II)

- 2 Alligator clips

- 1 Shoulder strap

- 1 Set of rechargeable batteries (Z502H)

- 1 Battery charger Z502R

- 1 Condensed operating instructions

- 1 Supplement Safety Information

- 1 DAkkS calibration certificate

- 1 USB cable

Product Code: M535C (M520N)