Product Descriptions

Profitest PVSun Memo

Tester for PV Modules and Strings per DIN EN 62446 (VDE 0126-23)

With the PROFITEST PVsun, all required electrical safety tests at photovoltaic systems can be executed simply and safely in accordance with DIN EN 62446.

The test instrument is suitable for testing PV modules and strings with up to 1000 V / 20 A. In addition to insulation measurement, polarity testing and ground fault testing, protective conductor continuity can also be tested. The tester is distin­guished by its ergonomic design and easy handling with a weight of only 500 g.