Product Descriptions

METRISO PRIME 10 Insulation Device

High-Precision Insulation, Low-Resistance and Voltage Measuring Instrument for up to 40 TΩ with 10 kV Test Voltage

The METRISO PRIME 10 insulation tester has been developed for the detection of insulation damage and for protection against electric shock in electrical power supply networks.

It measures resistance up to 40 TΩ with a test voltage of 10 kV in accordance with EN 61557-2. Even in the case of high-frequency interference, absolutely precise measurement results are obtained. Faults can be quickly and easily pinpointed by means of localization with the new "pulse control" function. Insulation measurements such as PI, DAR, DD, stepped testing (SV), capacitance measurement, temperature measurement and measurement of protective conductor continuity are no problem. These measurement results can be graphically represented at the display immediately.

Highlights

- Insulation measurement up to 40 TΩ with 10 kV test voltage in accordance with EN 61557-2 / VDE 0413-2

- Test voltages in fixed steps of 50, 100, 250, 500, 1000, 2500, 5000 and10,000 V

- Measurement with incrementally rising voltage

- Measurement of polarization index PI and absorption ratio DAR

- Measurement with shielded measurement cable

- Protection against voltage conducting objects

- Variable adjustment of limit values

- Digital filter for stabilizing measured values

- Creation of R/I or R/U diagrams

- Low-resistance measurement per EN 61557-4 / VDE 0413-4

- Continuity testing of protective conductors and equipotential bonding connections with a test current of ±200 mA

- Storage of test results

- Rugged IP 67 hard case

- Measuring category: CAT III 1000 V / CAT IV 600 V

Features

- Continuous display of measured insulation resistance or leakage current

- Automatic discharging of the device under test at the end of insulation testing

- Acoustic signal at 5 second intervals for quick generation of a characteristic time-resistance curve

- Adjustable measuring times of up to 99 minutes and 59 seconds

- Test times T1, T2 and T3 for measuring one or two absorption coefficients within a range of 1 to 600 seconds

- Polarization index (PI), absorption coefficients Ab1, Ab2, dielectric absorption ratio (DAR)

- Display of momentarily applied test voltage during measurement

- Test current: 1.2 / 3 and 5 mA

- Insulation testing by means of 2 or 3-wire method

- Measurement can be conducted using measurement cables with lengths of up to 55 meters

- Automatic measurement of multi-core cables with the optional AutoISO-5000 test adapter (max. voltage: 5 kV)

- Capacitance measurement during RISO insulation test

- Measurement of temperature with probe as accessory

- Dielectric discharge (DD)

- Fault localization with pulse control mode

- Adjustable limit values for measured resistance values for RISO and RPE

- Measurement of leakage current during insulation test

- Direct and alternating voltage measurement from 0 to 750 V

- Graphic representation of insulation resistance at the display during measurement

- Memory structure with storage of measuring points, systems and customer data

- 5.6" LCD display with background illumination

- Keyboard illumination

- Mains operation or with rechargeable lithium-ion battery

- Internal quick charger

Product Code: M555A