Product Descriptions

MetraHit World Multimeter

TRMS Digital Multimeter with Analog Bar Graph, Temperature Measurement and Infrared Interface

The autoranging multimeter for use in all areas of electrical engineering, in particular for international use.

The METRAHIT WORLD provides you with all of the measuring functions you'd expect from a versatile, world class multimeter: convincing technology with all voltage, resistance, current and temperature measuring ranges, and lots of other measuring functions and automatic features such as frequency and duty cycle measurement.

Resolution: 6000 digits (3 6/7 place) and analog bar graph (60 points)

Basic accuracy: 0.5% VDC

Bandwidth, V AC TRMS: 2 kHz

Patented automatic blocking sockets (ABS)

Voltage: VDC 100 μ to 1000 V and VAC TRMS 100 μ to 1000 V

Current: IDC 10 μ to 10 A (16 A 30 sec.) and IAC TRMS 10 μ to 10 A (16 A 30 sec.)

Resistance: 100 mOhm to 40 MOhm

Temperature: -50.0 to +800.0° C, type K thermocouple

Frequency measurement: 0.1 Hz to 1 MHz

Duty cycle measurement: 2% to 98% (1 kHz)

RPM measurement: 60 RPM to 99.99 thousand RPM

Capacitance measurement: 10 pF to 400 μF

Continuity and diode testing: 3 V

Min-Max measured value storage and DATA hold

DAkkS calibration certificate included as standard feature

Measuring category: 600 V CAT IV, 1000 V CAT III

Product Code: M206A