Product Descriptions

MetraHit IM Xtra All-in-One

All-in-One: Multimeter and Milliohmmeter, Insulation Measuring Instrument, Coil Tester, Data Logger

Well suited for service and diagnostics for electric machines and systems, in particular in the automotive industry, in electric machinery manufacturing and in aviation technology.

Compact and multifunctional for use in the field. Can be used advantageously in aircraft cockpits as well as in other constricted spaces, which would otherwise require the use of several individual instruments.

Product Highlights

- Milliohm measurement using 4-wire connection (Kelvin measurement) with 200 mA or 1 A

- Insulation tester with test voltage from 50 to 1000 V

- Coil test with 1000 V test voltage

Your Advantages

- Safety-relevant tests for electric devices, drives and installations with a single field instrument

- Testing of high-voltage systems in accordance with UN ECE R100

- Insulation resistance measurement per EN 61557-2 / VDE 0413-2

- Rlow installation testing per EN 61557-4 / VDE 0413-4

- Bonding test and equipotential bonding measurement, e.g. on aircraft outer skins (lightning protection, wick test)

Special Features - All-in-one Instrument

- Multimeter, insulation tester and milliohmmeter

- 4-wire milliohm measurement in a handheld instrument with 200 mA and 1 A

- Handheld instrument for field use with short-circuited coil detection at 1 kV

- Interfaces: Bluetooth, WIFI and USB

- Including DAkkS calibration certificate

Scope of Delivery

- 1 METRAHIT IM XTRA multimeter with rubber holster

- 1 test probe with START and STORE functions

- 1 pair of type KS17-2 safety measurement cables with 4 mm test probe

- 1 pair of type KC4 Kelvin clips

- 1 quick-change, rechargeable lithium polymer battery with micro USB charging socket

- 1 USB mains power pack (5 V DC, 2 A) with cable including micro USB charging plug

- 1 IZYTRON.IQ Business Starter software

- 1 set of condensed operating instructions, German/English

- 1 set of operating instructions in German and English (download)

- 1 DAkkS calibration certificate

- 1 hard case for the multimeter and accessories

Country of Origin: Germany

Product Code: M273S