Product Descriptions

GPS-2100+ Series Function Generator

The designs in the modern day can often be complex, demanding a variety of stimulus signals during test. The GPS-2100+ encompasses a number of clever circuitry techniques to make sure signals are accurately re-produced.

Benefits of EasyPulse© technology

- EasyPulse shows no one-reference-period-jitter compared to standard DDS generators

- Low jitter -- less than 100ps cycle-cycle RMS jitter

- At a frequency of 1Hz, the generator can output a pulse with a rapid rising/falling edge (6ns), however, the ordinary DDS pulse edge is very slow at the millisecond level.

- At 0.1Hz pulse, Easypulse edge can have a wide range of adjustment; the minimum edge is 6ns and the maximum edge can be adjusted to 6s. The ordinary DDS pulse edge adjustment is more restricted.

Features

- Dual-channel, with bandwidth up to 60 MHz, and amplitude up to 20 Vpp

- 150 MSa/s sampling rate, 14-bit vertical resolution, and 16 kPts waveform length

- Innovative EasyPulse© technology, capable of generating lower-jitter Pulse waveforms, brings a wide range and extremely high precision in pulse width and rise/fall times adjustment

- Special circuit for Square wave function, can generate Square waves up to 60 MHz with jitter less than 300 ps+0.05 ppm of period

- Plenty of analog and digital modulation types: AM, DSB-AM, FM, PM, FSK, ASK, PSK and PWM

- Sweep and Burst functions

- Harmonics Generator function

- Waveform Combining function

- High precision Frequency Counter

- Standard interfaces: USB Host, USB Device (USBTMC), LAN (VXI-11)

- Optional interface: GPIB

- 4.3" TFT-LCD display