Product Descriptions

MetraHit 27EX Milliohmmeter for Use in Potentially Explosive Atmospheres

Milliohmmeter for Use in Potentially Explosive Atmospheres

Compact milliohmmeter for the measurement of low value contact resistance in potentially explosive atmospheres, for example at contacts inside aircraft fuel tanks (bonding test), as well as for general low value resistance measurements inside and outside of potentially explosive atmospheres, for example on aircraft outer skins (lightning protection and wick test).

- Measuring ranges: 30 mΩ, 300 mΩ, 3 Ω, 30 Ω

- Resolution: 10 μΩ

- Measuring method: Kelvin connection (4-wire measurement)

- DATA Hold memory: 1200 measured values

- EX designation: Ex II 2 G EEx ia IIA T4

- Prototype test certificate: INERIS 05ATEX0040

- DAkkS calibration certificate

- Guarantee: 3 years material and workmanship

Product Codes:

M227F - Metrahit 27EX

M227G - Metrahit 27EX (AIRBUS için)