Product Descriptions

DUSPOL Digital 1000 Voltage Tester

Suitable for electrical engineering, industry, maintenance and service (troubleshooting)

- Voltage from 1 - 1000 V AC TRMS / 1200 V DC (LCD)

- Display levels: 50, 120, 230, 400 V AC/DC (LED)

- Backlit double display for displaying frequency (small display) and voltage (large display) or resistance

- Optical continuity test up to 100 kΩ (yellow LED)

- Resistance measurement: 0.1 kΩ - 300 kΩ (LCD)

- Diode test: 0.3 - 2 V (LCD)

- Phase sequence test (green LED) / phase test (red LED)

- Polarity test (LCD)

- Frequency measurement: 1 - 1000 Hz

- Direct display without key acknowledgment (high impedance testing)

- Load switched via pushbutton (high impedance testing)

- Intentional tripping of the RCCB

- Vibration alarm in the tester handle

- Illumination of measuring points and display

- IP65 protection (dust-proof / protected against water jets)

- Rugged housing design with rubberized handle

- Overvoltage category: CAT IV 600 V, CAT III 1000 V

- Includes two 1.5 V AAA batteries (LR03) (voltage display as of 50 V even with dead batteries!)

- Tested and approved in accordance with DIN EN 61243-3, VDE 0682-401:2011-02

Product Code: M611F