Product Descriptions

Metrahit PM-Prime Digital Multimeter

Precision TRMS Multimeter with Remote Control via Bluetooth, ± 310,000 Digits

The device is the successor to METRAHIT PRIME with identical data.

Precision multimeter, optionally with integrated Bluetooth, temperature measuring instrument and data logger for demanding, universal applications in the lab and for service calls

- Triple display with a resolution of ±310,000 digits

- Intrinsic error: ± (0.02% rdg. + 20 digits)

- Measuring functions:

- 1 µV to 600 VDC and 10 µV to 600 VAC/AC+DC TRMS (bandwidth: 15 Hz to 100 kHz),

- 1 nA to 10 ADC and 10 nA to 10 AAC/AC+DC TRMS (bandwidth: 15 Hz to 10 kHz)

- Resistance, frequency, capacitance and temperature measurement

- 1 mΩ to 30 MΩ, 0.001 Hz to 1 MHz, 1 pF to 3 mF, °C/°F,

- Pt100, Pt1000, type K thermocouple: -270 to +1372 ºC

- Automatic range selection and battery cutoff

- Min-Max measured value storage

- Integrated 2 MByte measurement data memory

- for approx. 300,000 measured values, sampling rate: 100 ms to 9 hrs.

- IR data interface

- CAT IV @ 300 V or CAT III @ 600 V per IEC 61010-1

- DAkkS calibration certificate as standard feature

- Power pack (optional)

Product Code: M248A, M248B (Bluetooth)