Product Descriptions

Programmable 350W Electronic Load (SPL series)

SPL series electronic loads are high-precision direct current sinks for use in research, product development, production, service and vocational training.

Four types are available with 200 until 400 W input power. The devices are distinguished by a diverse range of functions and excellent regulating accuracy, as well as outstanding ease of operation.

- 4 operating modes: constant current, constant voltage, constant load and constant power

- High-speed sequence and transient measurement, short-circuit proof, battery discharging and other auxiliary functions

- Minimum operating voltage is less than 0.6 V (80 V models)

- or 1.2 V (200 V models) at maximum current load

- Programmable current rise and fall time, steep edges

- Several groups of parameters (device settings) and sequences (load profile) can be saved and retrieved.

- Floating power input / no grounding

- Safe electrical separation

- Input can be switched on and off

- Voltage or current control is possible with constant power

- Settings selected by means of a rotary switch and keypad

- Multifunctional LCD panel

- Safety functions, amongst others adjustable power limiting

- Benchtop instrument, also suitable for mounting to a 19" rack

Product Code: K855A