Product Descriptions

SYSKON P3000 Programmable Laboratory Power Suplies

Series SYSKON (SYSTEM KONSTANTERs) are manual and remote controllable DC power supplies for laboratory and system use.

The power output is voltage and current controlled with limiting to maximum withdrawable power

Core Applications

- Testing of electrical and electronic components

- Executio of electrical test pulses, e.g. for automotive applications

- Execution of long-term testing

- Incorporation into test systems (with analog or digital control)

- Power Supply for sensetive devices, e.g. laser controllers

Functionality:

- Very short response times: <2ms

- Very high setting resolution: 1mV, 1mA 1ms

- High setting and measuring accuracy:0.05% + 30mV

- Extensive protective functions: overvoltage, overcurrent, overtemperature, limits

- Flexible programmability: large memory module, import/export of stored sequences and settings

- Power factor correction for sinusoidal current consumption

- Sensing terminals for auto-sensing operation at the power consumer

- Load resistance display

- Min-max values display

- Master-slave connection (series and parallel connection)

Scope of Delivery

- CD with user and driver software, operating instructions (D+EN), datasheet (D+EN)

- Clear-cut user software (soft front-panel)

- Mains power cable

- USB cable

- Installation set for 19" rack mounting

- DAkkS calibration certificate

- Operating instructions (printed)

Optional Accessories

- IEEE 488 arayüz

- IEEE 488 bus cable

- RS 232 bus cable

Product Code: K363A