Product Descriptions

MetraHit 2+ Multimeter

The METRAHIT 2+ provides users with all the measuring functions of a highly diverse multimeter: convincing technology with all voltage, resistance, current and temperature measuring ranges, and additional measuring functions and automatic functions.

Product Highlights

Resolution: 6000 digits (3 6/7 place) and analog bar graph

TRMS measuremnts VAC and IAC

Basic accuracy: 0.5% VDC

Patented automatic blocking sockets (ABS)

Voltage: VDC 100µ to 600 V and VAC 100µ to 600 V

Current: IDC 10µ to 10 A (16 A 30 sec.) and IAC 10µ to 10 A (16 A 30 sec.)

Resistance: 100 mOhm to 40 MOhm

Temperature: -200.0 to +400.0° C, type K thermocouple

Frequency measurement: 0.1 Hz to 1 kHz

Continuity and diode testing

Min-Max measured value storage and DATA hold

DAkkS calibration certificate included as standard feature

Measuring category: 600 V CAT III

Product Code: M205A