Product Descriptions

MetraHit IM E-Drive All-in-One

All-in-one: multimeter, milliohmmeter, insulation measuring instrument, coil tester and data logger for hybrid and electric drives

The METRAHit IM E-DRIVE BT is multimeter, milliohmmeter, insulation measuring instrument, coil tester and data logger in one. Applications include service and diagnostics for electric machines and systems, in particular in the automotive industry, in electric machinery manufacturing and in aviation technology.

An all-in-one instrument with 30,000 digits: milliohmmeter, multimeter, data logger, insulation resistance tester and coil tester.

Compact and multifunctional for use in the field: can be used advantageously in aircraft cockpits as well as in other constricted spaces, which would otherwise require the use of several individual instruments.

Product Highlights

- Milliohm measurement using 4-wire connection (Kelvin measurement) with 200 mA or 1 A

- Insulation tester with test voltage from 10 to 1000 V

- Coil test with 1000 V test voltage

Your advantages

- Safety-relevant tests for electric devices, drives and installations with a single field instrument

- Testing of high-voltage systems in accordance with UN ECE R100

- Insulation resistance measurement per EN 61557-2 / VDE 0413-2

- Rlow installation testing per EN 61557-4 / VDE 0413-4

- Bonding test and equipotential bonding measurement, e.g. on aircraft outer skins (lightning protection, wick test)

Applications

The multimeter is a portable, extremely rugged instrument designed for use in the field. It's suitable for maintenance, service and diagnostics at electric machines, drive units and systems, for example in automotive, avionics, energy and automation applications.

The all-in-one instrument combines an insulation tester, a milliohmmeter, a coil short-circuit tester and a universal multimeter. It's ideal for safety testing and diagnostics at electric and hybrid vehicles, as well as all types of electric machines.

In combination with an optional coil test adapter, it permits the measurement of short-circuited coils.

Country of Origin: Germany

Product Code: M274S