Product Descriptions

MetraCell BT Pro Mobile Battery Tester

Mobile test instrument for evaluation, maintenance and inspection of battery systems and uninterruptable power supplies (USP).

Mobile battery tester for voltage measurement; measurement for the electrical internal resistance and the electrochemical impedance of a battery block; capacity test via logging of current values and voltage curves; integrated Bluetooth interface, integrated IrDA interface for connecting a DMA35 density sensor, RFID transponder function.

The METRACELL is a mobile and multifunctional test device for the evaluation and maintenance of battery systems and uninterruptible power supplies (UPS), for example in computer centres, hospitals or power stations. Due to its small size, the measuring device can be easily attached to the technician's belt or worn around the neck on the enclosed belt. The METRACELL can be used to measure the voltage as well as the electrical resistance and electrochemical impedance of a battery block. Capacity tests can be conducted through logging of current vaulues and voltage curves. The device stores up to 30,000 data records, which can be managed with the supplied battery management software and output as CSV in the form of informative reports

Product Highlights

Safe

- Compact and shock-proof due to ABS housing and rubber holster

- User guidance easy to use before, during and after the test

- CAT III 600V DC

Reliable

- Rct and Rel measurement methods: possible electrical and electro-chemical damage to the battery block is reliably detected

- Battery operation: Up to 10 hours operating time

- Large internal memory: 300,000 records can be stored

- Voltage measurement: Designed for single and block voltage measuring up to 600V DC

- Capacity test: recording of discharge current and voltage curve

Flexible

- Additional measurements: Inclusion of all relevant parameters through optional accessories:

- Current

- Temperature

- Acid density

- Software: display, backup and logging of all measured values

- RFID Scanner: Use of RFID chips for fast data acquisition possible

- Data transfer: transfer of battery databases is possible

Your advantages

- Battery tester with:

- internal resistance measurement

- Voltage measurement up to 600V DC and 300 V AC

- Charge and discharge current measurement plus logging of voltage curves

- Temperature measurement

- acid density density data can be imported

Scope of Delivery

- 1 METRACELL BT PRO

- 1 Rubber holster

- 1 Power supply

- 1 Multimeter test probe KS 29

- 1 Carrying strap

- 2 Crocodile clamps

- 2 Kelvin probes for 4-wire measurement

- 1 Transport case

- 1 Test record / factory calibration certificate

- Includes: Battery management Software

Optional accessories:

- Current clamp CP1800

- Temperature sensor METRATHERM 2

- Acid density meter DMA35

Product Code: B100B