Product Descriptions

Metrahit Coil Multimeter with Interturn Short-circuit Detection and Insulation Test

The METRAHIT COIL multimeter is a rugged portable measuring instrument for use in the field.

The instrument is well equipped for universal electrotechnical use in the fields of service, diagnostics and electrical safety, in particular with regard to electric motors and is equipped with an internal, mains-independent power supply.

Product Highlights

- Insulation resistance measurement up to 3.1 GΩ with interference voltage detection - test voltages: 50 V, 100 V, 250 V, 500 V, 1000 V

- Interturn short-circuit detection with COIL Test Adapter (included)

- Multimeter with diverse functions (V, Ω, F, Hz)

- TRMS measurements: TRMS AC / AC+DC for current / voltage up to 10 kHz

- Activatable low-pass filter, 1 kHz / -3 dB in the V AC range

- Direct current measurement, 100 nA to 10 A

- Current measurement with current sensor clamps

- - A transformation ratio of 1 mV : 1 mA to 1 mV : 1 A can be selected and is taken into consideration at the display.

- Precision temperature indicator, °C or °F,

- for Pt100 / Pt1000 sensors and type K thermocouples

- Diode measurement (IK = 1 mA, Uflow to 5.1 V) and continuity testing

- Display: ±3,000 digits (3¾ place), illumination can be activated

- ±30,000 digits (4¾ place) at VDC and mΩ maesurements

- Acoustic signals for: continuity testing, dangerous contact voltages, exceeded overload limits

- Min-Max value storage

- Data memory and internal clock, power pack adapter socket

- IP 54 Housing protection, dust and splash protected, protective cover

- Bidirectional infrared interface for exchanging data with a PC

- Windows software available as accessory for processing and graphic display of measured values via RS 232 interface

Delivery

- 1 Insulation multimeter METRAHIT ISO or METRAHIT COIL

- 1 Protective rubber cover

- 1 Pair of safety measurement cables with 4 mm test probes, 1000 V CAT II, 600 V CAT III (KS17-2)

- 1 Condensed operating instructions, English/German

- 1 Operating instructions in English and German (CD ROM)

- 1 DAkkS calibration certificate

- 2 Batteries, 1.5 V, type AA, installed

- 1 COIL TEST ADAPTER for interturn short-circuit measurement (only in combination with METRAHIT COIL)

Product Code: M246C