Product Descriptions

AFV-P Series AC Power Source

AFV-P Series is a programmable AC power source with DC output and precision measurement. This compact power source provides clean power with THD less than 0.3% at 50/60 Hz and it delivers output voltage of 0-310 V and frequency of 40-500Hz (opt. 15-1000 Hz). It is ideal for commercial, defense and aerospace test applications from quality assurance, design verification, ATE to mass production.

Key Features

- Compact and high power density: 600VA to 2500VA is only 2U and 5000VA is 4U.

- AC source with DC output: extend the applications to DC testing.

- Wide output voltage of 0-310V and output frequency of 15-1000Hz.

- THD is only under 0.3 % when output power is under 100 Hz.

- Ideal for inrush current: capable to deliver up to 4.5 times of peak current.

- Start/End phase angle: users can define the start and end phase angle from 0° to 360°.

- Current foldback feature: have output current maintain constant based on the load which output voltage varies.

- STEP and RAMP function: ideal for voltage and frequency variation tests and effectively reduces the inrush current during motor startup.

- TRANSIENT generation provides users an easy setup for power line disturbance (PLD) simulation.

- Free control software and LabVIEW driver: allow users to easily program and remote control.

- Users can quickly set and view the parameters via 5 inches touch panel or rotary knob, which provides an easy operation and measurement display.

High slew rate: less than 300 μs from 0~90% output voltage.Specifications

Output Power

- Single Phase: 600VA / 1250VA / 2.5kVA / 5kVA

Specifications

Output Voltage

0~155V (Low Range)

0~310V (High Range)

0~620V (opt.)

Output Frequency

A ver.: 15~1000Hz

B ver.: 40~500Hz

THD

≦ 0.3% at 40~100Hz, ≦ 0.5% at 101~500Hz, ≦ 0.8% at 501~1000Hz (Resistive Load)

Load Regulation

≦ 0.07% F.S. (Resistive Load)

Crest Factor

≧ 3

Inrush Current

≧ 4.5 times of max.output current (rms)

Response Time

≦ 300 μs

DC Output Voltage

0~210V / 0~420V

Input Voltage

AFV-P-600 & AFV-P-1250: 98~132VAC / 196~264VAC

AFV-P-2500 & AFV-P-5000: 196~264VAC

Input Frequency

47~63Hz

Interfaces

Standard: RS232 / RS485 / Ethernet / USB / PLC Remote In&Out

Optional: GPIB / Analog Control

Dimensions (HxWxD)

AFV-P-600 & AFV-P-1250: 88 x 442 x 495 mm

AFV-P-2500: 88 x 442 x 650 mm

AFV-P-5000: 176 x 442 x 665 mm

Weight

AFV-P-600: 16kg (35.3lbs)

AFV-P-1250: 20kg (44.1lbs)

AFV-P-2500: 31.3kg (69lbs)

AFV-P-5000: 61.5kg (135.6lbs)

Product Code: Please contact us.