Product Descriptions

Metrahit CAL Universal Calibrator and Simulator

The METRAHIT CAL calibrator functions as a highly accurate calibration and simulation instrument for electrical quantities.

As a handheld instrument, it's suitable for precise, on-site calibration and inspection tasks, as well as for test department and laboratory work, in process engineering, control room and equipment fabrication, general measuring technology and many other applications.

Universal calibrator, simulator

mA, mV ...V, 5 ...2000 Ω, °C / °F

Pt100 / 1000, Ni100 / 1000,

- Thermocouples: J, L, T, U, K, E, S, R, B, N

- Frequency and pulse run generator: 1 Hz ...1000 Hz

- Ramp and staircase functions

- Easy operation

- Interface and optional METRAwin90-2 calibration software

- Transmitter simulator: sink: 0 ...24 mA

- DAkkS calibration certificate included as standard feature

- Rugged, EMC compliant design

Delivery

- 1 METRAHIT CAL calibrator with 2 batteries per IEC LR6

- 1 Pair of safety measurement cables (yellow and black) (1.5 m) with 4 mm test probes, 1000 V CAT III, 600 V CAT IV

- 1 Abbreviated operating instructions

- 1 CD ROM with operating instructions in English and German

- 1 Protective rubber holster

- 1 DAkkS calibration certificate

Product Code: M244A