Product Descriptions

Metraline Iso-Check 1000 V Insulation Tester

Insulation Measuring Instrument

The measuring instruments enables you to take measurements of the insulation resistance with test voltages of 50 to 1000 V - per VDE 0413-1,-2 (EN 61557-1,-2).

This with a measuring range of 100 kΩ through 1 GΩ.

Applications

- Measurement of insulation resistance at voltage-free devices and systems, up to 1000 V depending upon variant

- Measurement of surge protection devices, up to 1000 V depending upon variant

- Checking of test objects for absence of voltage

Features

- Insulation resistance measurement with test voltages of 50 to 1000 V

- Voltage measurement up to 600 V

- Measurement of surge protection devices with test voltages of 50 to 1000 V

- Table of common varistors can be displayed

- Digital display, backlit color OLED display

- Indication of dangerous touch voltage

- LED for measurement point illumination

- Patented means of securing test probes

- Compact and rugged: For service calls under harsh conditions and laboratory use

Product Code: M507C