Product Descriptions

KE7100 LANcheck LAN Tester

The KE7100 LANcheck is an easy to use, handy and cost-effective LAN Tester. The little brother of the KE7200 Ethernet Performance Tester is ideal for measurements in networks where documentation is not required or necessary.

- Wire-mapping & precise fault location

- Integrated cable database starting from 1 pair telephone incl. Profinet

- Measures cable lengths up to 150 m (TDR)

- Power over Ethernet test according to IEEE802.3af/at standard

- HUB-Blink and trace tone signal

- Master and Remote over voltage protected up to 100 V

Overview

The KE7100 tests the wires and wire pairs of the cable for continuity, open, short, inter-change and overdraft (Split Pair) and simultaneously determines cable length and distance to the fault in short circuit and interruption testing.

With the internal user-configurable cable database, unknown cable and wiring schemes belong to the past. Up to 32 individual remote units can be managed from the KE7100 simultaneously.

The device checks connections on the availability of Power over Ethernet (PoE and PoE +) and determines the available power.

Identifying data ports with the port finder function activates the link-LED on the switch and the integrated trace tone signal allows using the optional PROBE310 for cable tracing. The KE710x sets are the perfect help for installations and troubleshooting in telephone and data networks.

Product Code: KE7100