Product Descriptions

KE7200 Ethernet Performance Tester

The KE7200 Ethernet Performance Tester is an easy-to-use tool that verifies and troubleshoots all types of Ethernet cable installation, from essential copper wiring tests to active IP Ping. Advanced copper test capabilities include active TDR for cable length measurement and detection of split pairs even on jumpers (down to 2 meters). The KE7200 even shows multiple faults simultaneously.

- Wire-mapping and precise fault location

- Integrated cable database starting from 1 pair telephone incl. Profinet

- Recognition of branches (Bridge Taps) - optional

- Measures cable lengths up to 200 m (TDR)

- Power over Ethernet test according to IEEE802.3af/at standard

- Tests LAN using static IP or DHCP up to 1 Gbit

- List of active LAN devices and continuous ping test

- Master/Remote overvoltage protected up to 60 V AC

- Stores data and print out of test reports

Overview

The KE7200 Ethernet Performance Tester is the ideal tool for commissioning tests, troubleshooting and documentation in networks with an outstanding price/performance ratio. Versatile functions, the large graphical display and intuitive operating enable the user to work efficiently. Long battery life and a rugged housing are the perfect conditions for daily use.

The KE7200 tests the wires and wire pairs of the cable for continuity, open, short, inter-change and overdraft (Split Pair) and simultaneously determines cable length and distance to the fault in short circuit and interruption testing.

With the internal user-configurable cable database, unknown cable and wiring schemes belong to the past. Up to 32 individual remote units can be managed from the KE7200 simultaneously. The device checks connections on the availability of Power over Ethernet (PoE and PoE +) and determines the available power.

Active network tests such as the speed detection up to 1 GBit/s of the network connection, listing the existing network subscribers with Name, IP and MAC address as well as the configurable ping stress test with detailed statistics, information on the network and possibly faulty components.

Identifying data ports with the port finder function activates the link-LED on the switch and the integrated trace tone signal allows using the optional PROBE310 for cable tracing. The KE720x sets are the perfect help for installations and troubleshooting in telephone and data networks.

The supplied Ethernet Manager Software allows to create measurement reports and to maintain cable tests and network information.

Product Code:

D720A - KE7200 Ethernet Performance Tester

D723A - KE7200 Pro Kit Ethernet Performance Tester