Product Descriptions

CEM DT-812 Mini Infra Red Thermometers

CEM Mini Series Infra Red Thermometer is a very handy device to be used for all trouble-shooting engineers for taking temperature of areas that are inaccessible, moving targets and for surveillance of heat at various points in an area. These have fixed emissivity of 0.95 that covers 90% of the various materials whose temperature is measured.

These have Distance to sighting ratio of 8:1. This means that from a distance of 8 inches the area whose temperature is being measured would have a diameter of 1 inch. Therefore if the target has a diameter of 2 inches the maximum distance from where the temperature can be measured would be 2 x 8 i.e. 16 inches.

The instrument has a Red Laser marker through which the user can pin point the target whose temperature is to be measured.

- Precise Non Contact measurements

- Built in Laser Pointer

- User Selectable Degree C / Degree F

- MAX/MIN temperature Display

- Trigger Lock

- Automatic Data Hold & Auto Power Off

- Automatic Selection Range and Display Resolution 0.1 Degree C (0.1 Degree F) The meter at 8 inches away measures 1 inch target I Backlit LCD Display

Product Code: DT-812