Product Descriptions

Profitest Mtech+ IQ EV Basic Paket

Test Instrument Set for Testing Electric Charging Points

"EV Basic Package TECH+ IQ" test instrument set with PROFiTEST MTECH+ IQ, METRALINE PRO-TYP EM I and accessories required for testing electric charging points.With the "EV Basic Package MTECH+ IQ", you're well equipped for testing AC charging points for correct function and electrical safety.

Product Highlights

- Testing of AC/DC sensitive RCDs

- Testing of RCDs used specifically in electric charging points

- Testing of low-impedance continuity

- Testing of insulation resistance

- Vehicle, cable and fault simulation in a single instrument

- Testing of wall boxes with permanently attached charging cable

Your advantages

- Specific accessories for testing electric charging points

- Complete test sequence for safe and simple test procedures

- Extensive documentation of measured values and test results

Applications

The test instrument set is suitable for testing stationary electrical installations, in particular wall boxes, charging points and charging stations.

Single and 3-phase charging points can be tested for correct function and electrical safety in accordance with:

- IEC 61581-1 (DIN VDE 0122-1)

- IEC 60364-4 (DIN VDE 0100-600)

- EN 50110-1 (DIN VDE 0105-100)

Delivery

Test Instrument

1x PROFiTEST MTECH+ IQ

1x PRO-A3 II plug insert

1x PRO-SCHUKO plug insert

1x Compact rechargeable battery pack

1x Charger

Accessories

1x METRALINE PRO-TYP EM I test adapter for electric charging points

1x IZYTRONIQ Business Professional intelligent test software

1x Sortimo L-BOXX 238

1x L-BOXX PROFiTEST M insert

1x Protective gloves

1x variable plug adapter set

1x set of test probes, CAT III 600V

1x set of operating instructions

Product Code: M536S